## Slide 1
From Airwaves to Audio Files
The Physics and Mathematics of Digital Audio Sampling
Understanding the Nyquist Theorem, ADC Pipelines, and Quantisation

## Slide 2
The Core Challenge: Continuous vs. Discrete
Physical Reality: True sound is an analog pressure wave, infinitely variable in both time and amplitude.
Digital Reality: Computational architectures only process binary code (discrete 0s and 1s).
The Bridge: Sampling acts as the mathematical and electrical link, slicing continuous waves into distinct numerical frames.
Information Integrity: The process must capture enough detail to allow exact wave reconstruction without raw data bloat.

## Slide 3
The Architectural ADC Pipeline
Acoustic Input: Physical sound pressure waves vibrate a microphone diaphragm, generating low-voltage electrical signals.
Pre-Amplification: The low-voltage microphone signal is boosted to a clean, usable line-level hardware voltage.
Anti-Aliasing Filter: A low-pass hardware filter violently strips away all frequencies above the chosen system limit.
The ADC Chip: The core integrated circuit handles both Sampling (chopping time) and Quantisation (chopping amplitude).
Storage & Packaging: The resulting structural binary stream is written directly into uncompressed .wav file containers.

## Slide 4
Step 1: Time Discretisation (Sampling)
Definition: Measuring the exact instantaneous voltage of an analog signal at uniform, highly precise intervals of time.
Sampling Interval (Ts): The fixed, unvarying time duration separating consecutive signal measurements.
Sampling Frequency (fs): The total number of snapshots captured per single second, measured strictly in Hertz (Hz).
Mathematical Transformation: Maps a continuous-time signal x(t) into a discrete sequence defined as x[n] = x(nTs).

## Slide 5
The Nyquist-Shannon Sampling Theorem
The Fundamental Rule: To perfectly reconstruct an analog signal, the sampling rate (fs) must be greater than twice the highest frequency component (fmax) contained within the signal.
The Formula: fs >= 2 * fmax
Nyquist Frequency: The absolute mathematical frequency ceiling of a digital system, equal to exactly half the sampling rate (fs / 2).
Reconstruction: If this condition is met, the original wave can be rebuilt with zero mathematical loss or structural interpolation errors.

## Slide 6
The Penalty of Failure: Aliasing
Under-sampling: Occurs when a sound wave changes faster than the digital system is configured to sample it (fs < 2 * fmax).
Spectral Folding: The high-frequency wave reflects back across the Nyquist limit, impersonating an artificial low-frequency wave.
Digital Distortion: Creates harsh, metallic noise that is permanently baked into the data stream and cannot be filtered out later.
Prevention: The hardware anti-aliasing filter forces strict compliance by cutting off illegal high frequencies prior to conversion.

## Slide 7
Real-World Engineering: Why 44.1 kHz?
Human Biological Limits: The healthy human auditory system can perceive frequency vibrations up to roughly 20,000 Hz (20 kHz).
The Nyquist Baseline: According to the theorem, capturing human hearing requires an absolute minimum baseline of 40 kHz.
The Transition Band: The extra 4,100 Hz provides critical breathing room for physical, real-world analog filters to roll off efficiently.
Industry Standardization: Established during the early digital audio era to sync seamlessly with global video formats.

## Slide 8
Step 2: Amplitude Discretisation (Quantisation)
The Axis Split: While sampling slices the horizontal axis (Time), quantisation slices the vertical axis (Voltage Level).
Bit Depth (Resolution): The exact number of bits dedicated to expressing the numeric value of each individual sample point.
Resolution Scale Levels:
  - 16-Bit (CD Quality): Provides 2^16 = 65,536 distinct numerical amplitude steps.
  - 24-Bit (Studio Master): Provides 2^24 = 16,777,216 distinct numerical amplitude steps.
Quantisation Error: The tiny mathematical rounding offset between the true wave voltage and the nearest grid line. This error generates a permanent low-level noise floor.

## Slide 9
Pulse Code Modulation (PCM) & WAV Files
PCM Generation: The sequential stream of quantised integers is encoded directly into a continuous digital bitstream.
WAV Container Architecture:
  - Header Chunk: Defines critical file identity parameters: sample rate, bit depth, and channel configurations (Mono/Stereo).
  - Data Chunk: A massive, uncompressed sequential block of raw binary data representing audio amplitude over time.
Data Rate Formula: Bit Rate = Sample Rate * Bit Depth * Number of Channels
  - CD Calculation: 44,100 Hz * 16 bits * 2 channels = 1,411.2 kbps constant data throughput.

## Slide 10
Conclusion: Key Engineering Principles
Time Domain Mastery: Elevating the sample rate extends the system's ability to record higher frequencies cleanly.
Amplitude Domain Mastery: Increasing the system bit depth drops the noise floor and expands total operational dynamic range.
Mathematical Perfection: When Nyquist criteria are fully satisfied, digital audio does not lose information—there are no jagged 'staircases' in the final output wave.